## Slide 1: Simple SIMD Processor.
Group 4
EEE 4232 – VLSI II Project
Tanvir Hoque - 180205041
Avishek Debnath - 180205014
Akfa Sultana Mithika - 180205005

## Slide 2: TABLE OF CONTENTS SYNTHESIS 03 INTRODUCTION 01 DESIGN OF ALU 02 PNR AND VERIFICATION 04 CONCLUSION & FUTURE OUTCOMES 05

## Slide 3: INTRODUCTION
SIMD stands for Single Instruction Multiple Data. It is a type of parallel processing technology used in computer architectures to perform the same operation on multiple data elements in parallel. SIMD instructions allow a CPU to process multiple data elements in parallel within a single instruction cycle, increasing the overall performance and efficiency of the system.
SIMD technology is widely used in applications such as image and video processing, scientific simulations, and cryptography, where large amounts of data need to be processed in parallel. Many modern CPUs, including those based on the x86 architecture, support SIMD instruction sets, such as SSE and AVX.
This project is to implement a simple SIMD processor, core of which is a 16-bit SIMD ALU. 2's compliment calculations are implemented in this ALU. The ALU consists of three SIMD basic computation units: SIMD adder, SIMD multiplier and SIMD shifter.

## Slide 4: DESIGN OF ALU SIMD MULTIPLIER SIMD SHIFTER SIMD ADDER
The SIMD multiplier is implemented with adders and shifters. To make it support multiplication with different data width, the input signal, H, O and Q, are used to control the input operands of the adders and select corresponding outputs for the target data width.
The SIMD shifter can also support data with different width. It is based on two 16-bit shifters and necessary overstep-correct logic.
The SIMD adder is implemented based on 4 4-bit adders. To reuse the adder for data with different width, the input signals, H, O and Q, control the forwarding of the carries between the adders.

## Slide 5: SYNTHESIS
Fig1: Constraint tables
Fig2: Schematic view
Total No. of gates | 2885
Dynamic Power | 313.707 nW
Leakage Power | 1383115.097 nW

## Slide 6: PNR
Fig: Floorplan
Fig: PowerPlan
Fig: Pin Placement
Fig: Placement

## Slide 7: PNR
Fig1
Static Time Analysis
Fig2
Fig1 is the summary of existing setup and DRV violations in the pre-CTS stage. In the summary report, there is a negative value in max_tran which indicates that there is a violation.
So, to solve this violation optDesign –preCTS command is used in encounter terminal for optimization.Optimized summary reports is in fig2.

## Slide 8: PNR
Clock Tree Synthesis
After optimizing the design in placement stage, clock tree is needed to built in the design for balancing clock skew and latency. It is built using a clock buffer or inverter cells.

## Slide 9: PNR
Routing
Pre-CTS optimization is done in placement stage and after then we built the clock tree in CTS stage.Now, we need to perform detailed routing.

## Slide 10: PNR
Post-Route Timing Optimization
Previously, we check the summary report of existing setup and DRV violation on pre-CTS stage, now we will check it for routing stage.
Summary of existing setup and DRV violations
Summary of Hold violation

## Slide 11: PNR
Post-Route Timing Optimization
We tried to clean existing setup and DRV violations in post-route stage which summary report is in fig1 and also tried to clean hold violation which summary report is in fig2.
fig1
fig2

## Slide 12: PNR
To fill any spaces between regular library cells, Filler cells are used. After adding filler cells and then re-route the design the final design will look like this:

## Slide 13: Physical Verification
Name of verification | No. of violations
DRC | 5
Connectivity | 0
Geometry | 0
Antenna Rule Check | 0
PG short | 0
Power Via | 0
Stacked Via | 0
AC Limit | 0

## Slide 14: CONCLUSION & FUTURE OUTCOMES
An SIMD processor can be fabricated through many ways. We tried to synthesis this IC by the use of cadence tools and verilog codes. Although the design was slower than a hard-wired design, the development time for an application using this IC will be significantly lower since designers can adopt a purely programming based model and need not be concerned with lower levels details such as data path design, control design, hardware patterns etc.
An SIMD processor can be applied to the RC4 key search problem and able to achieve a high level of parallelism as well as utilize the higher memory bandwidth available on the device. The SIMD approach also has benefits in that the design can be amortized over many different applications potentially resulting in a large overall savings in development effort. Finally, using this approach, there is potential to customize the instruction set of the processor as well as to add coprocessing elements to further accelerate application.

## Slide 15: THANK YOU

## Slide 16: REFERENCES
Y. Fujita, S. Kyo, N. Yamashita, and S. Okazaki. A 10 GIPS SIMD Processor for PC-based Real-Time Vision Applications Architecture, Algorithm Implementation and Lan- guage Support. In In Proceedings of the 4th International Workshop of the Computer Architecture for Machine Per- ception, (CAMP), pages 22–32, Washington, DC, USA, October 1997. IEEE Computer Society
H. Fatemi, H. Corporaal, T. Basten, R. Kleihorst, and P. Jonker. Designing Area and Performance Constrained SIMD/VLIW Image Processing Architectures. In Proceed- ings of Advanced Concepts for Intelligent Vision Systems (ACIVS), pages 689–696, Antwerp, Belgium, September2005. Springer-Verlag, Berlin, Germany, 2005. K. Elissa, “Title of paper if known,” unpublished.
https://github.com/zslwyuan/Basic-SIMD-Processor-Verilog-Tutorial